## Slide 1
Duckiebot Grid Navigation
A* route planning, lane following, and obstacle avoidance on a real robot
Duckietown course project | robot duck4 | TUM
Notes: Goal: give the robot a start tile, a facing and a destination, and have it drive there on its own. Three parts: plan the route, follow the lane, handle what gets in the way.

## Slide 2
The task
Tell the robot where it is, which way it points, and where to go.
It must then reach the destination with no further help: staying in its lane, stopping at every red line, turning the right way at each intersection, and getting around anything in the road.
7 x 6
tile map
5
intersections
1980
routes verified
The map. Red marks the five intersections where a decision is made.
Notes: The map has 30 drivable tiles. Only five are intersections. Everything else is curves and straights the robot simply drives.

## Slide 3
How the pieces fit together
BROWSER
map_ui.html
click start, facing,
destination
>
PLANNER
a_star.py
route becomes an
ordered turn list
>
ROBOT
navigator.py
drives the route
on duck4
>
HARDWARE
camera + ToF
lane lines, red lines,
range ahead
One HTTP contract, unchanged
POST /navigate {"commands": ["right", "straight", "left", "stop"]}
GET /status POST /abort POST /follow
The robot serves the interface a teammate had already defined, so the app needed no changes. It also serves the planner page itself.
Notes: Everything talks over one small HTTP interface that was already agreed inside the team. The robot even serves the planner page, so it opens from any machine on the network.

## Slide 4
Planning: the state is not just the tile
A route made of tiles cannot tell left from right.
Search over (row, col)
Gives an ordered list of tiles
Says nothing about which way the robot faces
Cannot be turned into commands
Search over (row, col, facing)
Compare facing in with facing out
One step clockwise is a right turn
The turn list falls straight out
!
Commands are emitted only at the five intersections. Curves and straights are driven by lane following, so a command for one of those would shift every later turn onto the wrong junction.
Checked on all 1980 routes: every plan is well formed, and no plan contains a U-turn.
Notes: This is the single most important design decision in the planner. Heading has to be part of the search state, otherwise a path is just a set of tiles and you cannot derive turns from it.

## Slide 5
Lane following: a bug the road itself caused
On right-hand curves the robot steered left, into the oncoming lane.
Cause
A Duckietown road has a white edge line on both sides. Searching the whole image width, the far edge line of the oncoming lane was averaged in, dragging the computed lane centre to the left.
Fix
Look for each line only where it can legitimately be
Yellow centre line on the left, our white edge on the right
If white lands left of yellow it is the wrong line, so discard it
MEASURED
before lane centre 199 px, left of image centre 320 -> steers left on a right curve
after lane centre 319 px -> steers right, correct
A second fix mattered as much: when both lines briefly leave view mid-curve the robot now holds its turn instead of straightening, because straightening is what carried it out of the lane.
Notes: Worth stressing that the bug was not in the control maths. The controller was fine; it was being fed a lane centre computed from the wrong line.

## Slide 6
Intersections: stop timing the turn
no
Timed rotation
A tight right and a wide left need different amounts of rotation, and it varies by junction. No single set of timings worked.
yes
Rotate until a lane appears
The robot creeps in, then turns until it sees a lane ahead again. It stops rotating when it is actually lined up.
EACH TURN
1
Creep into the junction
2
Rotate until a lane is ahead
3
Hand back to lane following
Result: the same code drives a tight right and a wide left, with no per-junction timing table.
Only the creep distance is still set by hand, and it differs per direction: a tight right rotates earlier than a wide left.
Notes: The lesson generalises: replace an open-loop timing you cannot tune with a closed-loop condition you can observe.

## Slide 7
Obstacle avoidance: what did not work
The duckies are the same colour as the centre line, so colour just finds the line. We tried shape instead.
Chart: Same lane markings, consecutive frames
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Measured elongation of lane dashes | 1.6 | 2 | 2.3 | 1.2 | 1.5 | 1.3 | 1.4 | 1.7 | 2.2 | 2.4 | 2.3 | 1.4 | 1.6 | 1.1 | 1.1 | 1.3
Decision threshold | 1.9 | 1.9 | 1.9 | 1.9 | 1.9 | 1.9 | 1.9 | 1.9 | 1.9 | 1.9 | 1.9 | 1.9 | 1.9 | 1.9 | 1.9 | 1.9
Why it fails
A lane dash is a solid rectangle, so it fills its bounding box just as well as a duckie does.
Perspective squashes a nearby dash into a near-square blob.
The same markings read 1.1 to 2.4 across consecutive frames.
It also broke what worked. Misclassified dashes were erased from the mask to protect the steering, which left nothing to steer by. Lane following itself failed.
Notes: This is a negative result and it is worth presenting honestly. The chart is real logged data from the robot. The point is that elongation is not a stable property of these objects, so no threshold on it can work.

## Slide 8
Obstacle avoidance: measure distance, not colour
A duckie stands up and returns a short range. Flat tape on the road does not.
DETECT
0.35 m
close enough to be worth going around
CLEAR
0.50 m
the gap is hysteresis, so a reading on the limit cannot chatter
SWERVE
closed loop
the steering target slides across the centre line and back
The detector never touches the vision pipeline
A bad range reading cannot corrupt the centre-line measurement that steering depends on, so the failure mode from the camera attempt is structurally impossible.
A previous TUM batch reached the same conclusion: Duckietown-Btown used the same range sensor, and the team that stayed with the camera trained a neural detector instead.
Notes: Mention that we checked what earlier batches did before rebuilding. Nobody solved this with classical colour or shape vision, which supports the choice.

## Slide 9
Driving it: click two tiles
Click the tile the robot is on
Set which way it faces. Invalid headings grey out, because a corner tile cannot be faced every way.
Click the destination
Press send
The page runs the same A* in the browser and is served by the robot itself, so it opens from any machine on the network with nothing to configure.
Cross-checked against the Python planner on all 1980 routes: identical output.
start
end
right > straight > left > straight > stop
Notes: Demo this live if the robot is available. Otherwise walk through the map: click, set facing, click, send.

## Slide 10
What the project taught us
1
Put the right thing in the state
A path over tiles cannot express a turn. Adding heading to the search state made the command list fall out for free.
2
Prefer a condition you can observe
Turns became reliable the moment rotation ended on seeing a lane rather than on a stopwatch.
3
Check the measurement before the algorithm
No amount of threshold tuning fixes a reading that is not stable. Changing sensor solved in one step what three detectors could not.
4
A fix must not endanger what works
The camera detector broke lane following. Its replacement was deliberately kept out of the vision path.
Notes: Keep this slide short when presenting. These four lessons are the transferable part of the project.

## Slide 11
Limits, and what comes next
Known limits
The robot stays in sync with the plan by counting red stop lines. One missed line makes every later turn wrong.
Stop lines are ignored during a swerve, so an obstacle must not sit right before a junction.
Colour thresholds depend on the lab lighting and are re-tuned with a slider tool.
The robot's base software is newer than the course release, so the official demo will not run on it. Our stack bypasses it entirely.
Next steps
1
AprilTags at each junction, so the robot knows which intersection it is at instead of counting
2
Use the range sensor for a stop-and-wait behaviour as well as a swerve
3
Close the loop on turns with the wheel encoders
Notes: Counting stop lines is the biggest remaining fragility and AprilTags are the standard answer. Say that we scoped them out deliberately in order to get the whole route working end to end first.

## Slide 12
Two clicks to a route
Plan, follow, turn, avoid, arrive.
Questions
Notes: Offer a live demo if the track is set up.